## Slide 1: Automotive Radar
GET BATCH 2 AM ADAS

## Slide 2: Table of contents 01 04 02 05 03 06
Intro
Radar signal processing 1
ADAS and AD
Basics of Radar
Radar signal processing 2
Radar Data Processing
RADAR
TECHNOLOGY

## Slide 3
It is the term used for systems which assist / help drivers to increase the safety of the passengers , drivers and other road users while driving the vehicle. (say, car, Truck, etc)
ADAS ( Advanced Driver Assistance Systems)
How does ADAS Work?
By providing visual Information
By providing visual and/or audio warning in case of danger situation
By interfering the vehicle motion
Example :
Adaptive Cruise Control (ACC)
Rear Cross Traffic Alert (RCTA) System
Vehicle Exit Alert System
Automatic Parking
Traffic Sign recognition

## Slide 4
Levels

## Slide 5
General Working of ADAS and AD
Both ADAS (Advanced Driver Assistance Systems) and AD (Autonomous Driving) systems are kind of Automation systems having different levels of Autonomy.
All these systems can be in generally described using below block diagram.

## Slide 6
Sensors in ADAS
There are 2 types of sensors:-
Exteroceptive Sensors:-(Camera, LIDAR,RADAR, etc)
Proprioceptive Sensor:-(GPS, IMU, ENCODERS, etc)
Advantage of Radar over other sensor :

## Slide 7
Radio – uses Electromagnetic waves in Radio spectrum
Detection – detect Objects/targets like plane, car, pedestrian, etc
Ranging – calculates the range (distance) of the target from sensor
Radar
Basic working of Radar
Radar is used to collect the information related to the object or target by radiating electromagnetic energy and examining the echo received from the distant object.

## Slide 8
Based on Signal processing
Classification of Radar
Based on Applications
Primary
Secondary
CW
Pulse
Unmodulated
Modulated
MIT
Doppler
Surveillance
Tracking Radar
Imaging Radar
Meteorological Radar
Automotive
Radar altimetry
Air Traffic
Air Defence

## Slide 9
Automotive radars serve the purpose of identifying the speed and distance of objects in the surrounding area of the vehicle.
Short Range Radar (50m)
Medium Range Radar (80 – 100m)
Long Range Radar (250 – 300m)
Why FMCW?
Continuity of Measurement
Range Resolution
Maximum Range Requirement
Power requirement
Automotive Radar

## Slide 10
A point reflection of electromagnetic wave from the object.
Detection points :
Range
Azimuth
Elevation Angle
Doppler Speed
RCS (Radar Cross Section)
Probability of detection Pd: The Pd probability that the receiver output exceeds the threshold and the target is present.
Probability of missing Pm: The probability that the received voltage is below the threshold but the target is present.
Probability of false alarm Pf : The probability that the received voltage exceeds the threshold but the target is not present.
Automotive Radar Measurement

## Slide 11
For short-range radar, the 24 GHz NB and UWB bands have been in use in legacy automotive sensors.
Due to spectrum regulations and standards developed by the European Telecommunications Standards Institute (ETSI) and the Federal Communications Commission (FCC), the UWB of 24GHz can`t be used in Automotive Industry.
High Bandwidth leads to high range resolution of the Radar Sensor. Hence Frequency of 77 GHz.
76 GHz - 77 GHz -> for Long Range Radar Applications, Adaptive Cruise Control, Collision avoidance, etc.
77 GHz – 81 GHz -> for SRR and MRR Applications, Blind spot detection, Rear cross traffic alert, etc.
From 24 GHz to 77 GHz in Automotive Radar

## Slide 12
Protects radar from outer dust, water and harsh weather.Made with material which minimally attenuates the RF signal.
Inside an Automotive Radar
Case for the complete sensor which holds all the internal circuit and parts together. Provides protection to the sensor and allows the easy handling for people.
Contains multiple pins inside, where combination of certain pins are dedicated to each separate interface. Helps during predevelopment, testing and final production of sensor.
Includes Transmitting and Receiving antennas.
Analog in behaviour.
Digital part of the sensor.
Contains the power supply Unit for the sensor and other DSP electronics.
Part of the Radar case / Body.
Helps to protect Radar circuit and make it easy to handle.

## Slide 13
Radar Sensor on vehicle
Ego vehicle, target vehicle and coordinate system

## Slide 14: Sensor coordinate system
Need for ego coordinate system
We need one coordinate system which can be used as reference for measurement and comparison of all the sensor data.
Depending on application, we can use either only 2D system or 3D system of coordinates
Can be define in same manner as ego coordinate system.
The origin will be then the place on ego vehicle where sensor is placed.

## Slide 15
Sensor field of view
Total area covered by sensor, where it can detect the objects.
Main parameters which governs FoV of Radar Sensor are
Minimum and Maximum vertical Range
Minimum and Maximum Horizontal Angle

## Slide 16: FMCW
Triangular waveform
(Upramp and Downramp)
- Frequency Modulated Continuous waveform
Sawtooth waveform
(Upramp or Downramp)

## Slide 17
The difference between the highest frequency and the lowest frequency of the signal.
One complete Ramp is called chirp. One frequency sweep from lowest to highest frequency
slope = delta(Y)/delta(X)
delta(Y) = Bandwidth (Fh - Fl)
delta(X) = Ts
therefore, slope = BW/Ts
Centre frequency between highest and lowest frequency component.
Bandwidth
Chirp
Chirp Time (Ts)
Total amount of time taken to start of the chirp to end of the chirp
Slope of the Chirp
Carrer Frequency
Segment or One frame
Total number of chirps in one scan of the Radar sensor. It sends continuous chirps one after another

## Slide 18
One chirp time(Ts) * Number of chirp.
Difference between the transmitted signal and received signal frequency
Time Segment
Intermediate Frequency
Rx signal is sampled to covert it from analog to digital. The frequency at which the sampling takes place is called chirp Sampling
Chirp Sampling
Measurement of Range
;
;
Resolution

## Slide 19
Measurement of Velocity
Radar uses the principle of Doppler shift to measure the velocity
The apparent change in the frequency of the wave due to the relative motion of the source and the observer is called Doppler shift.
IF = f1(distance) + f2(doppler shift) , but in automotive radar f2<<<<<f1, so f2 is discarded and can’t be calculated using IF.
We need to calculate the phase change of the two consecutive chirps
Maximum Velocity formula
More no. of chirps -> High resolution
Resolution

## Slide 20
Measurement of Angle
AoA :Phase difference between the two Rx signal receiver by Rx antenna.
Maximum Angle :
Resolution

## Slide 21
Measurement of RCS
Radar : It sends out radio waves.
Object : It could be of any shape and size, it reflects back some of the radio waves back to the radar.
So, Radar cross section is a way to describe how visible an object appears to radar, based on the shape and size.
Factors : Surface, shape, Material, Tx frequency etc.
RCS Large object > RCS small object
Corner Reflector : It is a retroreflector used for Radar testing and calibaration, consisting of three perpendicular intersecting flat surfaces

## Slide 22
Clutter
Unwanted reflection points in Radar Measurement is Clutter
Sources:
Ground Reflection.
Nearby Static objects which are not consider as valid target objects.
Rain, fog, some particles in air, etc.

## Slide 23
Why to remove Clutter ?
Unwanted reflection points in Radar Measurement is Clutter.
Clutter adds to a lot of extra measurements which is Unwanted.
Considerably decrease the useful information /feature extraction at higher level of processing.
Can lead to false activation of vehicle actuators during driving.
Example: Reflection from ground falsly detected as from vehicle, and ADAS brakes the vehicle for safety
How to remove Clutter ?
Every Radar Reflection has Magnitude / Received Power.
Use some threshold to filter based on this value

## Slide 24
Measurement of RCS
Radar : It sends out radio waves.
Object : It could be of any shape and size, it reflects back some of the radio waves back to the radar.
So, Radar cross section is a way to describe how visible an object appears to radar, based on the shape and size.
Factors : Surface, shape, Material, Tx frequency etc.
RCS Large object > RCS small object
Corner Reflector : It is a retroreflector used for Radar testing and calibaration, consisting of three perpendicular intersecting flat surfaces

## Slide 25
Measurement of RCS
Radar : It sends out radio waves.
Object : It could be of any shape and size, it reflects back some of the radio waves back to the radar.
So, Radar cross section is a way to describe how visible an object appears to radar, based on the shape and size.
Factors : Surface, shape, Material, Tx frequency etc.
RCS Large object > RCS small object
Corner Reflector : It is a retroreflector used for Radar testing and calibaration, consisting of three perpendicular intersecting flat surfaces

## Slide 26
Automotive Radar Data Processing
Section -6 Part I
Coordinate Transformation
Ego vehicle motion compensation
Separation of Dynamic and Static detections

## Slide 27: Image source : https://www.udemy.com/course/automotive-radar-basics-to-advance
Detection | Range (m) | Velocity (m/sec) | Angle (degree) | RCS | Other Parameter
1 | 20.5 | -6.5 | 10 | * | *
2 | 36 | 0.5 | 20 | * | *
… | …….. | …….. | …….. | ……. | ………………….

## Slide 28: Ego vehicle motion compensation
Relative vs Absolute velocity
Relative velocity = VB - V A
VAB = -90m/s (Doppler relative velocity)
Detected by the radar
-90m/s
40m/s
-50m/s
Absolute velocity = VAB + V A
VB = -50m/s (Absolute velocity)

## Slide 29: Coordinate Transformation
Transformation from Polar to Cartesian Coordinates:
x=r⋅cos(θ)
y=r⋅sin(θ)
Where:
r is the range (distance from the radar to the target),
θ is the azimuth angle (angle in the horizontal plane).
3D Transformation (Including Elevation):
z=r⋅sin(ϕ)
Where:
ϕ is the elevation angle.
Image source : Stochastic Geometry Methods for Modeling Automotive Radar Interference

## Slide 30: Transform Sensor – Ego vehicle
P’(r’,θ’) is the distance from Sensor reference.
x’ = r’⋅cos(θ’)
y’ = r’⋅sin(θ’)
P(r,θ) is the distance from Ego vehicle reference.
x = r⋅cos(θ) + r’⋅cos(θ)
y = r⋅sin(θ) + r’⋅sin(θ)
R^2 = x^2 + y^2
Where:
R is the range (distance from the ego point to the target),
θ is the azimuth angle (angle in the horizontal plane for ego point).

## Slide 31: Transform – Sensor to Ego Vehicle
Radar Detection before Transform | Radar Detection after Transform
Range (in sensor coordinates) | X in ego vehicle coordinates
Angle (in sensor coordinates) | Y in ego vehicle coordinates
Doppler Relative Velocity | Doppler Absolute Velocity
RCS | RCS
…………….. | ……………..

## Slide 32: Filtering of Dynamic and Static Detection
In ADAS and in AD, we are interested in all the moving objects around vehicle
To avoid collisions, and other danger situations
Only detections from moving objects are required to process
Filter using absolute Velocity of the detections
Absolute Velocity contains velocities only above certain threshold – say > (+/- 0.5 m/sec) - Dynamic
Image source : Mobileye & WNC collaborate on imaging radar | Mobileye News

## Slide 33
Clustering and Feature Extraction

## Slide 34
Feature Extraction Table

## Slide 35
Single Object Tracking

## Slide 36
Multi Object Tracking

## Slide 37
Prediction And Measurement Cycle

## Slide 38
Data Allocation In Mot

## Slide 39: Thank You!